Key characteristics of distributed system

Scalability:
with increase data scale, performance should remain the same

Horizontal Scale: increase number of server
Vertical scale: increase machine performance: ram, cpu,disk

software support:
horizontal scale: mongodb cassandra
vertical scale: mysql

Reliability:
ability to keep delivering service even some of them fail
this is achieve by redundancy

Availability:
the time system remains operational to perform its required function in a specific time

Efficiency:
how fast the system can response to your request
two standard to measure it:
1.response time or latency:delay of time to get the item
2.throughput or bandwidth:number of items delivered in a period of time

Client-Server Model: achieve by http, socket, go through DNS for ip query, in linux use tool like
 dig www.google.com

port should also be specific: like http for 80, https 443
linux command example: nc -l 8088 (server) nc 127.0.0.1 8088 (client)

Network protocol:
IP, TCP, HTTP

IP packet two main components:
ip header: (store in bytes include src, dst,total size, version v4/v6) 20-60 bytes
ip data: 2^16 bytes limit

if the data is large, how to do it? Divide into multiple packets, how to make sure reliable?

TCP to control:
tcp build on top of ip packet

For application usage, HTTP build on top of the TCP

Storage:
One main issue: persistence
two category: disk and memory

Load Balancer:
spread the traffic across a cluster of servers to improve responsiveness and availability of application
places you can add load balancer:
user and webserver
webserver and application server
application server and database server
Algorithms to use for balancer:
base line: choose the one which is healthy and can response the correct thing according to the request
types:
least connection method: use the ones with least number of active connection
least response time method: choose the lowest average response time ones
least bandwidth method: choose least Mbps ones
round robin method: when servers are equal specification and not many persistent connections
weighted round robin method: server assign a weight, a higher weight one get assigned
ip hashing: the hash of ip address of client is calculated and redirect

Problem with load balancer: single point failure of load balancer:
solution: redundant load balancer